## Slide 1
人工智慧與決策分析研究室 (AIDA)：
許嘉裕、莊佳臻
日期 : 2023/08/29
設備異常偵測模型於時間序列資料之研究
Constructing Anomaly Detection Model for
Time Series Data and Empirical Study

## Slide 2: Background
2
Introduction
Proposed method
Experiment result
Conclusion
The goal of this study is to establish a real-time anomaly detection model for DMS cleaning machines that will enable constant machine state monitoring.
The collected data lacks sufficient labels and is mostly comprised of normal state sample. Therefore, the construction of an anomaly detection model needs to be carried out using only normal state data.
Further losses may be effectively mitigated if problems are quickly identified and the proper actions are then implemented based on the relevant decision criteria.

## Slide 3
Situation description
3
Introduction
Proposed method
Experiment result
Conclusion
Situation |  | Challenge | Solution
Data collection | DMS cleaning machine Robot torque data 7 axis Collection frequency： once pre second | Insufficient labeled samples The utilized data only consists of samples in normal states. The data exhibits shifts in both time duration and torque magnitude Performing anomaly detection without sufficient labeling. | Utilizing unsupervised learning methods. Utilizing generative models for auxiliary modeling of normal state samples. Performing anomaly detection of various types using shape indicators, distribution indicators, and instantaneous indicators. Establishing a multi-faceted unsupervised anomaly detection framework.
Data characteristics | Single feature(torque) sequential data |  | 
Target | Real-time monitoring of DMS cleaning machine |  | 

## Slide 4
Execution Results
4
 | As-Is | To-Be | Benefit
生成資料混合訓練 | 設備異常的紀錄鮮少 | 生成正常樣本和真實數據資料進行混合訓練 | 使異常偵測模型能學習正常樣本完整之資料輪廓 改善決策邊界樣本的偵測能力。形狀指標漏檢率有8% - 63% 的下降，分佈指標下降15%-48%
異常偵測 | 傳統監督式學習方法 非監督式機器學習方法 | 使用非監督式深度學習框架LSTM-DAGMM，透過深度學習模型在學習時間序列資料非線性特徵同時擬合正常資料之資料分佈 將資料進行時域特徵之轉換，觀察序列在短時間變化之表現 | 非監督式學習無須進行資料標記 DAGMM透過深度學習之特性進行重構學習和密度估計的聯合優化。壓縮網路進行序列表現的學習，估計網路進行資料分佈之學習 時域轉換特徵捕捉正常狀態下瞬時變化之界線
 | 單一指標進行異常偵測 | 建構三種異常偵測指標進行偵測，DAGMM生成形狀指標以及分佈指標，瞬時指標由時域特徵轉換而成，由三種指標進行多面向異常偵測。 1.形狀指標：序列原始表現之異常 2.分佈指標：序列潛在特徵分佈之異常 3.瞬時指標：序列在短時間變化之異常 | 利用三種指標進行多面向之異常偵測，三種指標能夠互補相互不足的地方。和以往單一面向進行偵測的方法相比，準確率平均能達到9成
Introduction
Proposed method
Experiment result
Conclusion

## Slide 5
01
02
03
04
Content
Introduction
Proposed method
Experiment result
Conclusion

## Slide 6: DMS cleaning machine – data description
6
Introduction
Proposed method
Experiment result
Conclusion
Axis name | Collection time | Sample quantity | Sequence length(s)
TR UNIT | 2022/11/09-2022/11/15 | 4836 Samples | 55
LD UP Y |  | 3706 Samples | 26
LD UP Z |  | 3439 Samples | 50
LD LOW |  | 3528 Samples | 60
UL UP Y |  | 2580 Samples | 45
UL UP Z |  | 3578 Samples | 80
UL LOW |  | 3321 Samples | 20

## Slide 7
7
Propose Method – training stage
Introduction
Proposed method
Experiment result
Conclusion

## Slide 8
8
Propose Method – inference stage
Introduction
Proposed method
Experiment result
Conclusion

## Slide 9
Data Generation - Time-Series GAN
9
Supervised loss
Reconstructed loss
Unsupervised loss
Step 1.
Autoencoder component training
Step 2.
adversarial generation component training
Step 3.
Joint learning
Encoding learning
Data generation
Recovery network
Embedding network
Discriminant network
Generate
network
(Yoon et al. 2019)
Introduction
Proposed method
Experiment result
Conclusion

## Slide 10
Anomaly Detection - DAGMM
10
Compression network
Dimensionality reduction and low-dimensional feature space construction.
Output：sequence similarity and latent space feature .
Estimation network
Density estimation via reconstruction error and low-dimensional features.
Output：Mixed composition .
DAGMM optimizes the learning of dimensionality reduction and density estimation at the same time by joint training.
( Zong et al. 2018)
Where sequence similarities are :
Introduction
Proposed method
Experiment result
Conclusion

## Slide 11
Monitor strategy
11
Instantaneous indicator：
( Time domain features similarity)
Distribution indicator：
( Estimation network )
Estimation network
Shape indicator：
( Compression network )
Time domain feature
Determine if the samples exhibit unexpected performance in the original space by MSE .
The calculation of the NLL. A higher value indicates a poorer match with the model.
Obtaining by Mahalanobis distance and time-domain features, determine small and short changes in series.
Introduction
Proposed method
Experiment result
Conclusion

## Slide 12
Time domain feature transformation |  | 
Statistic feature | Maximum | 
 | Minimum | 
 | Standard deviation | 
Sequence feature | p to p value | 
 | peak index | 
 | crest factor | 
 | clearance factor | 
 | shape factor | 
 | impulse factor | 
……
Set mean as central by feature
Instantaneous indicator
Mahalanobis distance calculation
……
Time domain feature
Monitor strategy - instantaneous indicator
Introduction
Proposed method
Experiment result
Conclusion

## Slide 13
Monitor strategy – integrated index
For each indicator :
If indicator exceed threshold  indicator score = 1
For example :
Shape indicator：
If shape indicator exceed threshold  Shape score = 1
Else shape score =0
After score transformation, each indicator score will be concatenate as state array .
Where :
Introduction
Proposed method
Experiment result
Conclusion

## Slide 14
Monitor strategy – Anomaly value
 | Shape indicator | Distribution indicator | Instant indicator
Maximum | 0.0510 | 2.4985 | 0.0165
Thresh | 0.0109 | -21.40 | 0.0020
Minimum | 0.0030 | -23.1839 | 0.00005
 | Shape value | Distribution value | Instant value
Maximum | 1.0000 | 1.0000 | 1.0000
Thresh | 0.1759 | 0.0805 | 0.1274
Minimum | 0.0000 | 0.0000 | 0.0000
 | Shape value | Distribution value | Instant value | Integrated index
Normal | 0.0927 | 0.0042 | 0.0858 | 0
Thresh | 0.1759 | 0.0805 | 0.1274 | 0
Sample 1 | 0.0441 | 0.1269 | 0.0124 | 1
Sample 2 | 0.1172 | 0.0210 | 0.1478 | 1
Sample 3 | 0.3993 | 0.0969 | 0.6750 | 3
Sample 4 | 0.0156 | 0.0478 | 0.0808 | 0
Transformation：
Detection result：
Introduction
Proposed method
Experiment result
Conclusion

## Slide 15
Data description – LD LOW
15
 | TimeGAN | LSTM-DAGMM | 
Training set | 2943 | 5958 | 2943(real data)
 |  |  | 2943(TimeGAN)
Validation set | - | 445 | 
Test set | - | 704 | 
Sequence length | 60 | 60 | 
……
Torque sequence data
By robot operating cycle
Introduction
Proposed method
Experiment result
Conclusion

## Slide 16
Experiment design
16
Operation | factor
Standby | Belt
Carrying | Bearing Slider
Complexity | Belt & bearing Belt & slider
Based on the machine‘s operating principles and combined with normal signal data, design abnormal samples. corresponding to the following types of anomalies：
Contextual abnormality.
point abnormality.
sequence abnormality.
Point abnormality
Contextual abnormality
Sequence abnormality
Introduction
Proposed method
Experiment result
Conclusion
Choi et al., 2021; Blázquez-García, A et al
Choi et al., 2021; Blázquez-García, A et al
Choi et al., 2021; Blázquez-García, A et al

## Slide 17
Experiment design - Standby section abnormality
17
Loose belt
tightened belt
Standby section abnormality can be determined as Contextual abnormality.
Introduction
Proposed method
Experiment result
Conclusion

## Slide 18
18
Bearing loss
Slider loose
Carry section abnormality can be determined as point abnormality.
Sequence design：slider
Point design：bearing
Experiment design - Carry section abnormality
Introduction
Proposed method
Experiment result
Conclusion

## Slide 19
19
Loose belt & Bearing loss
Loose belt & Slider loose
tightened belt & Bearing loss
tightened belt & Slider loose
Complexity abnormality can be determined as sequence abnormality.
Experiment design - Complexity abnormality
Introduction
Proposed method
Experiment result
Conclusion

## Slide 20
Test data setting
20
Generate 1000 records for each type of anomaly based on their degree of severity.
Repeat the testing process 10 times and average the results for evaluation.
Testing set :
No. Normal data : 704
No. abnormal data :
Sample type | 
Normal | 704
Abnormal (total 8 type) | 100*8(each type)
Total No. sample | 1504
Each indicator use the 95th percentile of the training set results and fine-tuned with the validation
Integrated index threshold setting is 1.
 |  | prediction | 
 |  | Abnormal | normal
True | Abnormal | TP | FN
 | normal | FP | TN
Introduction
Proposed method
Experiment result
Conclusion

## Slide 21
21
Anomaly detection result - comparison
The proposed method has high accuracy, and the capability of capturing anomalies is significant, and also has the balanced performance.
The reconstruction-based autoencoders also showed good results, but its anomaly detection performance significantly differed from the proposed method.
The other methods, such as k-means based on DTW and the two-step GMM might have higher false negatives and false positives. The capability of capturing anomalies is significant decrease with proposed method.
Introduction
Proposed method
Experiment result
Conclusion

## Slide 22
Anomaly detection result - comparison
22
Reconstruction based :
  The reconstruction error is not significantly influenced by the rapid variations in shape and point anomalies, therefore the autoencoder has less ability to identify tightened belts and point anomalies.
Time series clustering ：
  DTW can better capture the temporal shifts. However, techniques using Euclidean distance as the benchmark performed worse in detecting all kinds of anomalies.
Two step method：
  The outcomes of these two techniques show the benefits of the suggested approach's use of DAGMM, which maximizes dimension reduction through joint training and supplies comprehensive information for subsequent density estimation.
performance metrics : Recall
Introduction
Proposed method
Experiment result
Conclusion

## Slide 23
Mixed data training result
23
Shape index result in Real data
Distribution index result in Mixed
Shape index result in mixed
Distribution index result in Real data
t-SNE result
Mixed training improves the detection of samples on the decision boundary.
Enhances the data profile of normal samples.
Optimizes the detection of anomalous samples near the boundary.
False Negative(FN) result in mixed data
Introduction
Proposed method
Experiment result
Conclusion

## Slide 24
 | shape | distribution | instant
Loose belt | 0.8762 | 1.0000 | 0.9987
tightened belt | 0.7075 | 0.9962 | 0.9325
Bearing loss | 0.2087 | 0.4612 | 0.8750
Slider loose | 0.1600 | 0.2050 | 0.7875
Loose belt & Bearing loss | 0.9512 | 1.0000 | 1.0000
Loose belt & Slider loose | 0.9725 | 1.0000 | 1.0000
tightened belt & Bearing loss | 0.8212 | 0.9725 | 0.3487
tightened belt & Slider loose | 0.6350 | 0.9250 | 0.1962
Validity for each indicator
24
performance metrics : Recall
Introduction
Proposed method
Experiment result
Conclusion

## Slide 25
 | shape | distribution | instant
Loose belt | 0.8762 | 1.0000 | 0.9987
tightened belt | 0.7075 | 0.9962 | 0.9325
Bearing loss | 0.2087 | 0.4612 | 0.8750
Slider loose | 0.1600 | 0.2050 | 0.7875
Loose belt & Bearing loss | 0.9512 | 1.0000 | 1.0000
Loose belt & Slider loose | 0.9725 | 1.0000 | 1.0000
tightened belt & Bearing loss | 0.8212 | 0.9725 | 0.3487
tightened belt & Slider loose | 0.6350 | 0.9250 | 0.1962
Shape indicator
25
For two samples with the contextual abnormality, the shape of tightened belt is more similar to the normal sample. As a result, it effects the detection capability.
For point anomalies, which involve short and rapid changes, shape indicators have similar performance with the normal samples.
Loose belt
tightened belt
performance metrics : Recall
Slider loose
Bearing loss
Introduction
Proposed method
Experiment result
Conclusion

## Slide 26
 | shape | distribution | instant
Loose belt | 0.8762 | 1.0000 | 0.9987
tightened belt | 0.7075 | 0.9962 | 0.9325
Bearing loss | 0.2087 | 0.4612 | 0.8750
Slider loose | 0.1600 | 0.2050 | 0.7875
Loose belt & Bearing loss | 0.9512 | 1.0000 | 1.0000
Loose belt & Slider loose | 0.9725 | 1.0000 | 1.0000
tightened belt & Bearing loss | 0.8212 | 0.9725 | 0.3487
tightened belt & Slider loose | 0.6350 | 0.9250 | 0.1962
Distribution indicator
26
The distribution indicator is a model's measure of the latent representation of a sample in terms of its distribution, which involves observing the overall characteristics of the sequence. point anomalies have a less significant effect on the overall characteristics, making the distribution indicator less capable of detecting point anomalies effectively.
performance metrics : Recall
Slider loose
Bearing loss
Introduction
Proposed method
Experiment result
Conclusion

## Slide 27
 | shape | distribution | instant
Loose belt | 0.8762 | 1.0000 | 0.9987
tightened belt | 0.7075 | 0.9962 | 0.9325
Bearing loss | 0.2087 | 0.4612 | 0.8750
Slider loose | 0.1600 | 0.2050 | 0.7875
Loose belt & Bearing loss | 0.9512 | 1.0000 | 1.0000
Loose belt & Slider loose | 0.9725 | 1.0000 | 1.0000
tightened belt & Bearing loss | 0.8212 | 0.9725 | 0.3487
tightened belt & Slider loose | 0.6350 | 0.9250 | 0.1962
Instant indicator
27
Instantaneous indicator is designed to detect the occurrence of instantaneous anomalies, with a shortage for tightened belts and belt-slider anomalies. This may be because these two anomalies exhibit peak variations that are similar to normal samples.
performance metrics : Recall
Introduction
Proposed method
Experiment result
Conclusion

## Slide 28
DMS machine 7 axis mixed training result
28
 | Shape indicator |  |  | Distribution indicator |  | 
 | Real data | Mixed data | improvement | Real data | Mixed data | improvement
Axis 1 | 75 | 47(-28) | 37.3% | 519 | 534(+15) | 2.89%
Axis 2 | 236 | 103(-133) | 56.3% | 426 | 221(-205) | 48.12%
Axis 3 | 173 | 64(-109) | 63.00% | 406 | 258(-148) | 36.45%
Axis 4 | 234 | 207(-27) | 11.53% | 133 | 107(-26) | 19.54%
Axis 5 | 162 | 148(-14) | 8.64% | 594 | 503(-91) | 15.31%
Axis 6 | 10 | 4(-6) | 60.00% | 234 | 181(-53) | 22.64%
Axis 7 | 118 | 95(-23) | 19.49 | 582 | 585(+3) | 0.51%
performance metrics : Number of false negative
TimeGAN was used in this study to create samples of the normal condition. The generated samples and real data were combined and sent into the DAGMM for training.
1
2
This strategy reduced false negatives for shape indicator by 8% to 63% and for distribution indicator by 15% to 48%.
Introduction
Proposed method
Experiment result
Conclusion

## Slide 29
DMS machine 7 axis anomaly detection result
29
 | Clustering based | Reconstruction based | Two step method | Proposed method
Axis 1 | 0.5036 | 0.8861 | 0.6845 | 0.9232
Axis 2 | 0.7023 | 0.8617 | 0.7023 | 0.9657
Axis 3 | 0.7328 | 0.8809 | 0.5446 | 0.9117
Axis 4 | 0.5772 | 0.8077 | 0.7530 | 0.8806
Axis 5 | 0.5249 | 0.6596 | 0.6551 | 0.7294
Axis 6 | 0.8107 | 0.8575 | 0.7788 | 0.9709
Axis 7 | 0.6200 | 0.9005 | 0.5045 | 0.8978
performance metrics : Accuracy
1
In this study, a deep learning model was trained using both generated and real data. Two different types of indicators were produced by deep learning model, and a third type of indicator was created by using time-domain feature transformation.
This method improved in the comprehensive anomaly identification. The accuracy can average up to 90% over traditional single-faceted anomaly detection techniques.
2
Introduction
Proposed method
Experiment result
Conclusion
 | Clustering based | Reconstruction based | Two step method | Proposed method
Axis 1 | 0.5036 | 0.8861 | 0.6845 | 0.9232
Axis 2 | 0.7023 | 0.8617 | 0.7023 | 0.9657
Axis 3 | 0.7328 | 0.8809 | 0.5446 | 0.9117
Axis 4 | 0.5772 | 0.8077 | 0.7530 | 0.8806
Axis 5 | 0.5249 | 0.6596 | 0.6551 | 0.7294
Axis 6 | 0.8107 | 0.8575 | 0.7788 | 0.9709
Axis 7 | 0.6200 | 0.9005 | 0.5045 | 0.8978

## Slide 30
DMS machine 7 axis Recall
30
Introduction
Proposed method
Experiment result
Conclusion
 | Clustering based | Reconstruction based | Two step method | Proposed method
 | Recall | Recall | Recall | Recall
TR UNIT | 1.0000 | 0.9993 | 0.5508 | 0.9095
LD UP Y | 0.6376 | 0.9431 | 1.0000 | 0.9446
LD UP Z | 0.6711 | 0.9574 | 0.4357 | 0.8963
LD LOW | 0.5917 | 0.7442 | 0.6481 | 0.9687
UL UP Y | 0.5619 | 0.6123 | 0.6181 | 0.7785
UL UP Z | 0.9768 | 0.7346 | 0.6940 | 0.9908
UL LOW | 0.6539 | 0.8836 | 0.5254 | 0.8660
The study's data show differences in numerical magnitudes and temporal durations. As a result, in some axis, normal samples might be misunderstood for anomalies because of the shifting.
LD LOW
Improvements direction
Data Alignment
Considering Relevant Features
TR UNIT
UL UP Y

## Slide 31
DMS machine 7 axis Precision
31
Introduction
Proposed method
Experiment result
Conclusion
 | Clustering based | Reconstruction based | Two step method | Proposed method
 | Precision | Precision | Precision | Precision
TR UNIT | 0.3218 | 0.7807 | 0.6971 | 0.9477
LD UP Y | 1.0000 | 0.8201 | 0.6376 | 0.9895
LD UP Z | 0.9986 | 0.7840 | 0.5914 | 0.9403
LD LOW | 0.5285 | 0.9588 | 0.8953 | 0.8096
UL UP Y | 0.4275 | 0.9209 | 0.8934 | 0.6761
UL UP Z | 0.7457 | 1.0000 | 0.9663 | 0.9518
UL LOW | 0.6805 | 0.9488 | 0.5577 | 0.8480
This study also focuses on identifying anomalies that demonstrate significant changes. Therefore, further research will be needed to verify the proposed method's capacity to identify certain abnormalities, such as those demonstrating growing changes.
LD LOW
UL LOW
UL UP Y

## Slide 32
Conclusion
32
Introduction
Proposed method
Experiment result
Conclusion
Point abnormality
Contextual abnormality
Sequence abnormality
Sequence anomalies are anomalies that exhibit similar patterns but with different numerical values. Therefore, differences are more likely to be observed in terms of reconstruction error measurement and density estimation. It's important to note that in certain situations, the detection capability of density estimation methods might be weaker.
Contextual anomalies are anomalies that exhibit unexpected behavior within a sequence. Therefore, methods like clustering or density estimation are more likely to observe differences in such cases.
For point anomalies, it is recommended to use time-domain feature analysis and select appropriate features for analysis. It is worth noting that point anomalies with sufficiently distinct differences can also be distinguished using reconstruction-based methods.

## Slide 33
This study provides a multifaceted unsupervised learning-based anomaly detection framework, to address the problem of modeling anomalies in real-world situations where the process is restricted by a shortage of anomalous samples.
Conclusion
33
1
2
It is possible to improve the data profile of normal state by using generative models to generate different normal samples. False negatives reduced 8% to 63% for shape indicator, 15% to 48% for distribution indicators.
3
Instantaneous indicators overcome the shortcoming of shape and distribution indications in point anomalies. The shape and distribution indicators compensate for the instantaneous indicator‘s weaknesses in detecting complexity anomalies. Accuracy can average up to 90% .
Introduction
Proposed method
Experiment result
Conclusion

## Slide 34
Execution Results
34
 | As-Is | To-Be | Benefit
生成資料混合訓練 | 設備異常的紀錄鮮少 | 生成正常樣本和真實數據資料進行混合訓練 | 使異常偵測模型能學習正常樣本完整之資料輪廓 改善決策邊界樣本的偵測能力。形狀指標漏檢率有8% - 63% 的下降，分佈指標下降15%-48%
異常偵測 | 傳統監督式學習方法 非監督式機器學習方法 | 使用非監督式深度學習框架LSTM-DAGMM，透過深度學習模型在學習時間序列資料非線性特徵同時擬合正常資料之資料分佈 將資料進行時域特徵之轉換，觀察序列在短時間變化之表現 | 非監督式學習無須進行資料標記 DAGMM透過深度學習之特性進行重構學習和密度估計的聯合優化。壓縮網路進行序列表現的學習，估計網路進行資料分佈之學習 時域轉換特徵捕捉正常狀態下瞬時變化之界線
 | 單一指標進行異常偵測 | 建構三種異常偵測指標進行偵測，DAGMM生成形狀指標以及分佈指標，瞬時指標由時域特徵轉換而成，由三種指標進行多面向異常偵測。 1.形狀指標：序列原始表現之異常 2.分佈指標：序列潛在特徵分佈之異常 3.瞬時指標：序列在短時間變化之異常 | 利用三種指標進行多面向之異常偵測，三種指標能夠互補相互不足的地方。和以往單一面向進行偵測的方法相比，準確率平均達到9成
Introduction
Proposed method
Experiment result
Conclusion

## Slide 35
許嘉裕博士*、莊佳臻研究生
人工智慧與決策分析研究室(AIDA)
* cyhsu@gapps.ntust.edu.tw
設備異常偵測模型於時間序列資料之研究
友達光電 & 國立臺灣科技大學 產學合作研究

## Slide 36
THANK YOU

## Slide 37
DMS machine 7 axis anomaly detection result
37
1
2
Introduction
Proposed method
Experiment result
Conclusion
 | Clustering based |  | Reconstruction based |  | Two step method |  | Proposed method | 
 | Recall | Precision | Recall | Precision | Recall | Precision | Recall | Precision
TR UNIT | 1.0000 | 0.3218 | 0.9993 | 0.7807 | 0.5508 | 0.6971 | 0.9095 | 0.9477
LD UP Y | 0.6376 | 1.0000 | 0.9431 | 0.8201 | 1.0000 | 0.6376 | 0.9446 | 0.9895
LD UP Z | 0.6711 | 0.9986 | 0.9574 | 0.7840 | 0.4357 | 0.5914 | 0.8963 | 0.9403
LD LOW | 0.5917 | 0.5285 | 0.7442 | 0.9588 | 0.6481 | 0.8953 | 0.9687 | 0.8096
UL UP Y | 0.5619 | 0.4275 | 0.6123 | 0.9209 | 0.6181 | 0.8934 | 0.7785 | 0.6761
UL UP Z | 0.9768 | 0.7457 | 0.7346 | 1.0000 | 0.6940 | 0.9663 | 0.9908 | 0.9518
UL LOW | 0.6539 | 0.6805 | 0.8836 | 0.9488 | 0.5254 | 0.5577 | 0.8660 | 0.8480
Precision is the capacity to correctly identify normal events, while Recall is the capacity to detect anomalies. Performance on all axes is balanced for the proposed method.
On the other hand, other methods have a bias towards one of these metrics, which may lead to more false positives or false negatives in their identification.
Although the performance of the proposed method is mostly balanced, there are still some false negatives and false positives exist. In the following parts, this will be discussed in more detail.
3

## Slide 38
Conclusion
38
Introduction
Proposed method
Experiment result
Conclusion
False positive situation
False negative situation
The study's data show differences in numerical magnitudes and temporal durations. As a result, in certain cases, normal samples might be misunderstood for anomalies.
Improvements direction
Data Alignment
Aligning the data in a specific manner. It could potentially impact the results of model training.
Considering Relevant Features
The performance of the model could be improved by adding pertinent features to the estimation network of the DAGMM as well as the time-domain features.
The anomalous samples utilized in this study’s inference phase were produced by experimental design.
Certain samples may be labeled as anomalies by the definition after the addition of noise components, yet they may actually be normal samples.
This study also focuses on identifying anomalies that demonstrate significant changes. Therefore, further research will be needed to verify the proposed method's capacity to identify certain abnormalities, such as those demonstrating growing changes.